Longitudinal
Parameter	Role	Units	Typical range	Sample
b0	Shape factor		1.4 - 1.8	1.5
b1	Fz influence on longitudinal friction coefficient (*1000)	1/kN	-80 - +80	0
b2	Longitudinal friction coefficient (*1000)		900 - 1700	1100
b3	Curvature factor of stiffness/Fz	N/%/kN2	-20 - +20	0
b4	Change of stiffness with slip	N/%	100 - 500	300
b5	Change of progressivity of stiffness/Fz	1/kN	-1 - +1	0
b6	Curvature change with Fz2		-0.1 - +0.1	0
b7	Curvature change with Fz		-1 - +1	0
b8	Curvature factor		-20 - +1	-2
b9	Fz influence on horizontal shift	%/kN	-1 - +1	0
b10	Horizontal shift	%	-5 - +5	0
b11	Vertical shift	N	-100 - +100	0
b12	Vertical shift at Fz = 0	N	-10 - +10	0
b13	Curvature shift		-1 - +1	0

Coefficient	Name	Formula
C	Shape factor	C = b0
D	Peak factor	D = Fz·(b1·Fz + b2)
BCD	Stiffness	BCD = (b3·Fz2 + b4·Fz)·e(-b5·Fz)
B	Stiffness factor	B = BCD / (C·D)
E	Curvature factor	E = (b6·Fz2 + b7·Fz + B8) · (1 – b13·sign(σ+H))
H	Horizontal shift	H = b9·Fz + b10
V	Vertical shift	V = b11·Fz + b12
Bx1	(composite)	Bx1 = B · ( σ + H)

Lateral

Parameter	Role	Units	Typical range	Sample
a0	Shape factor		1.2 - 18	1.4
a1	Fz influence on lateral friction coefficient (*1000)	1/kN	-80 - +80	0
a2	Lateral friction coefficient (*1000)		900 - 1700	1100
a3	Change of stiffness with slip	N/deg	500 - 2000	1100
a4	Change of progressivity of stiffness / Fz	1/kN	0 - 50	10
a5	Camber influence on stiffness	%/deg/100	-0.1 - +0.1	0
a6	Curvature change with Fz		-2 - +2	0
a7	Curvature factor		-20 - +1	-2
a8	Fz influence on horizontal shift	deg/kN	-1 - +1	0
a9	Horizontal shift at Fz = 0 and camber = 0	deg	-1 - +1	0
a10	Camber influence on horizontal shift	deg/deg	-0.1 - +0.1	0
a11	Vertical shift	N	-200 - +200	0
a12	Vertical shift at Fz = 0	N	-10 - +10	0
a13	Camber influence on vertical shift, Fz dependent	N/deg/kN	-10 - +10	0
a14	Camber influence on vertical shift	N/deg	-15 - +15	0
a15	Camber influence on lateral friction coefficient	1/deg	-0.01 - +0.01	0
a16	Curvature change with camber		-0.1 - +0.1	0
a17	Curvature shift		-1 - +1	0

Coefficient	Name	Formula
C	Shape factor	C = a0
D	Peak factor	D = Fz · (a1·Fz + a2) · (1 – a15·γ2)
BCD	Stiffness	BCD = a3 · sin(atan(Fz / a4) · 2) · (1 – a5·|γ|)
B	Stiffness factor	B = BCD / (C·D)
E	Curvature factor	E = (a6·Fz + a7) · (1 – (a16·γ + a17)·sign(α+H))
H	Horizontal shift	H = a8·Fz + a9 + a10·γ
V	Vertical shift	V = a11·Fz + a12 + (a13·Fz + a14)·γ·Fz
Bx1	(composite)	Bx1 = B · ( α + H)